## Slide 1: Data handling in - understanding delays in networks - GNN in SDN

## Slide 2: Understanding delays in networks
390 provided datasets (always rawed traffic and delay matrix). Name: data{Topology}_{Ntotal}_{Nsend}_{rho_{max}}_16000_{TD}.txt
  Routing: 4 datasets with different routing algorithms
  Saturation: 220 datasets on a fixed network (scale-free, 10 nodes), intensity and traffic distribution changes
    Network topology and routing are provided in case of scale-free. Not defined if used in input
  Netsize: 3 datasets (5, 10, 15 nodes), fixed distribution, fixed intensity, variable number of nodes
  Topologies: 163 datasets on which number of nodes and traffic distribution changes
    Star topology: 51 datasets
    Ring topology: 52 datasets
    Scale-free topology: 60 datasets, also topology changes. Routing table and network is provided (as .ned)
  No code provided
Not clear if training has been done using only traffic and delay matrices or also with topology (.ned) and routing (routing table) as in GNN

## Slide 3: GNN in SDN
2045 provided datasets for traffic matrix and delay (always rawed traffic and delay matrix). Name: dGlobal_0_<lambda>_<routing_file>.txt
Traffic and delay
  Nsfnet (used for train and evaluation): 595
  Geant2 (only for evaluation): 690
  GBN (only for evaluation): 760
For every network they provide in input also the equivalent .ned and a routing table
  It seems the assumption of having topology and routing in input is fair because of their implications to saturation, as long as the model is able to generalize learning with different topologies and routings
  Can the routing table be computed online to simplify data by defining the algorithm (if deterministic)?
Code is provided
  At first they put data in tfrecords to improve performance
    This part also automatically extracts paths and links given topology and routing
  Message passing phase: extracts path_state features from T, D, paths and links
  Readout: training phase learns function relating path_state and delay, inference requires path_state
    So, also during inference topology and routing are required to convert these data into path_state

## Slide 4: Ns3
Simulation to obtain
  Network topology: required in case of GNN. Idea: tracing on the events that create nodes and channels
  Routing: required in case of GNN. Idea: tracing on events that implement routing
  Traffic matrix T. Used in form of average real bandwidth (not datarate) from node i to node j. Idea: tracing on packet send / received events to always sum
    Time that was needed to send the data (final result: total_time)
    Amount of data that was sent (final result: total_data)
    When to do total_data/total_time and store it as the element (I,j) of T?
    How to identify a tracing?
  Delay matrix D. Idea: tracing packet send / received events to always sum
    Time needed (final result: total_time)
    Number of packets (final result: total_packets)
    Compute delay per packet as total_time / total_packets
    Same doubts
Simulation must be divided in epochs and periods. One epoch will provide one traffic matrix, the periods in one epoch the average traffics and delays
  How to